Notes for the Introduction to Emergency Communications and

FRS Radios for CERT Tactical Communication

Class 1 of 2, December 12, 2013

Instructor Qualifications:

Using Handheld Radios (HT) for over 35 years.  Taught 100s of people on the job,

mostly by example, using radios in all kinds of conditions

Amateur Radio Operator K6JGZ

Started as a Tech at the request of the Fire Department

Used the ARRL Tech License book

QRZ.com/Resources/Practice/Amateur Radio Exams

QRZ ‘You are being called by” Q-codes

Used the ARRL General License book as reference

Finally realized how radios actually worked

Studied for General on my own because it was interesting and fun

Offered an Extra Class by Armando Montalvo KI6TAA								Ended up studying intensively daily for weeks.  And it worked.

Extra Class License with unlimited access to any of the many Amateur Radio Bands

GMRS License WQKX334

Volunteer firefighter in a rural/urban interface for 6 years in New Mexico where radio

propagation was difficult.

Currently volunteer for the LAFD Auxiliary Communications Service

Just completed a major LAFD EOC/DOC drill – 100 msgs per hour		Opened a lot of eyes of the Command Staff and the Outside Evaluators.

Objectives:

Introduction to Emergency Communications, not comprehensive.

More comprehensive resources available in handouts and on line.

What would you like to learn from this class?

Class Organization

No PowerPoint. (tend to read ahead and then zone out…)

Normally a two session classes

Second class is more hands messages and using radios.

Try to do this in one session?

Emergency Communications:

FEMA defines an emergency incident as a

“…planned or unplanned occurrence or event, regardless of cause, which requires action by emergency service personnel." to protect human life or immediate property damage.

http://www.fema.gov/emi/is195.htm . Section 1.9

How is “action by emergency service personnel” going to happen?

Pause

Communication – Emergency Service have to find out about it.

The emergency service personnel need to know:

What kind of incident?

Where is the incident?

What services and resources are needed?

Emergency communications consist of messages to and from the emergency communicator and emergency service personnel so appropriate action can be taken and resources provided.

Who provides the information?

Pause

You do.  Citizens do.

How do you do it?

Pause

Usually 911

Ever listened to a 911 call?

What did it sound like?

911 operators have to spend most of their time getting the caller to

calm down and prompt them for the necessary information

How much time could be saved if the caller knew Emergency

Communications – Minutes, maybe many minutes to get all the

necessary information.

How long for Brain Death?  Bleed out?  Placitas CPR Story

What are some other benefits of proper emergency communication?

911 operator realized they are talking to a rational, organized, communicator with

immediately useful information that is probably accurate and important.  You are speaking to them in a way they can immediately understand.  Everyone can start to get organized

Emergency communicators are those who have learned to communicate immediate necessary information concisely and accurately in a timely fashion to help “…prevent or minimize loss of life or damage to property and/or natural resources” regardless of the obstacles in the event.

Emergency communicators provide:

What happened?

Where it happened?

What is needed

Follow up with additional information as it becomes available.

What are the obstacles to good emergency communications?  (Pause)

Emotions

Excitement

Adrenaline

Magnitude of the event

Trauma/Horror of the event

Confusion

Noise

Panicked bystanders

Easy to get caught up in the moment

Cardinal Directions and Street names can be confused

Traffic - Wisconsin mass traffic collision with bystanders in the road.

Trip/Fall (French Barn Story) If injured, girl would be ground up in power takeoff

Fire/Electrical/Hazardous substances

Electrocuted good Samaritans in Studio City for a non-injury accident.

Injured responder becomes part of the problem – or THE problem

Good Emergency Communication is a skill

Not something an untrained person can conveniently figure out on the fly.

Untrained communicators use too many words and include unnecessary 			information which

Prevents fast action

What you initially want to talk about may not be the most useful

Information

NOT A CONVERSATION

It is specific information delivered in a concise timely manner

It’s a skill shared with the provider and the listener.

The communicator and receiver have a common understanding

Both the provider and the listener need to use critical thinking skills.

Takes a little practice and a lot of clear thinking

And takes a lot of listening

Easy to learn

Listen to Fire and Police radio

Broadcastify.Com

Scanner radios

Tell Placitas radio story of radio that wouldn’t transmit

Use short, concise messages - CLARITY

Think about what you want to say.

Find a concise way to say it.

25 words or less.  15 is better.

MVA with injuries NB 170 Burbank Offramp (10)

Cross street Burbank.(total 13)

55 year old female chest pain 11614 Riverside cross street Ben.

What are some examples?

Accuracy

Check the numerical location and the cardinal directions BEFORE you speak.

Have the correct street name OR indicate the area as precisely as possible

Salt Lake City Parley’s Canyon Paper Delivery story

Activate EMS before responding if possible

Make notes if necessary - Rehearse what you are going to say

What, Where, What is needed

Age, sex, principal complaint, mechanism of injury

No Privacy

No privacy.  Period.

Never use names, phone numbers, or patient ID.

Choose the best way to send your message

Cell Phone to IC or 911

Runners (2) with written notes

Kids on bicycles with notes

Radios

It’s the message that counts, not the medium.

What do you need to communicate?

Sizeup – VERY IMPORTANT

Absolutely Necessary for Good Emergency Communications.

Quickly and safely investigate the situation and gather preliminary information necessary for others to understand what may be going on.

(We could do a whole class just on Sizeup

What is wrong?

What needs to be done?

Who needs to do it?

How is the situation changing?

and

What has changed since the last transmission

What is the resolution?

What are you going to do next?

Why sizeup?  Your IC and other listeners finds out what is happening and can

plan a response

Report ONLY what you see and understand.  Do NOT GUESS or SPECULATE.

Make sure you fully size up the situation and update your situation as necessary.

Single Family residence – Smoke showing

Light plane crash in the back yard?

Motor Vehicle accident

Vehicle on top of an electrical vault? - Power lines in the water?

If the situation changes, sent an updated message.

And keep in touch – every 10 minutes or so.

Why would you use a radio in a disaster?

Only if no better communications mode is available

911 and/or cell phones may be better…

Force multiplier – one operator replaces two runners

Provides IC with more timely information.

Allows for two-way communication

Allows IC to allocate resources knowing a communicator is on scene.

Increased communication speed (vs. runners)

Safety

Why use FRS for CERT Tactical Communications?

Sophisticated device

Better than the extremely expensive HTs I started using in the 70s

KEEP YOUR MANUAL WITH THE RADIO

Inexpensive and readily available

No License necessary

Short Range

Works well at short distances (½ to 1 mile)

Operation Gratitude FRS example in Shuttle Story

This is an advantage, not a disadvantage

More channels open in your area

Less chance of interference from distant areas

Anything you hear will probably be in or near your

Neighborhood – Situational Aware ness

An FRS radio is not a cell phone

Shared resource – SHARED

When you’re using the frequency, no one else can

Doubling

Use short, concise messages

Think about what you want to say.

Find a concise way to say it.

Check the location and the cardinal directions BEFORE you speak.

Make notes if necessary - Rehearse what you are going to say

No privacy.  Period

Never use names, phone numbers, or patient ID

Biggest problems with any HT (Handie Talkie or Handheld):

Weak Batteries

NiCads wear out/out of condition – Have Alkaline standing by.

Don’t like to be partially charged

Condition your NiCads.  Completely discharge, recharge regularly

Keep fresh batteries in a safe container with the radio

Poor location – Higher - Away from Structures - Out of the car

Your finger

Pressing the PTT button when not taking

Not pressing the PTT when you do want to talk. (Death grip story)

Radio  Demonstration

FRS/GMRS Channels

PTT switch  Hi/Lo

FRS vs GMRS

FRS is available to all, without a license, and has enough power to be extremely

useful

GMRS has more power, but not that much more, and requires a license to operate legally - “Any radio frequency is legal in an emergency”  Wrong.

Privacy Codes:

“Locks” the radio to a select group of users using the same code.

Convenient for Disneyland, but not emergency situations

Interferes with tactical communications

Can’t tell if you are ‘doubling’ with another transmission

DON’T use privacy codes for emcomm – Ever

Prevent you from finding a clear frequency

Prevents you from hearing situational reports

Example of Northridge Train wreck:   LAFD all on specific tactical

Frequencies was able to monitor them all and report back to

the Staging Captain

Privacy Codes ON may cause you to ‘double’ with another communicator

Explain how to turn everything OFF

Location, Location, Location

Height trumps power

Direct TV example FRS 1/2w same as FRS (Armando Montalvo KI6TAA)

Line of sight trumps height (Palos Verdes flat tire story)

Power trumps everything else

Tactical Call Signs

Use Descriptive Unique Tactical Call Signs

NOT -- CERT 1, TEAM 1, etc.

BE SPECIFIC – Be UNIQUE -- Adams Street CERT 1, Adams Street Search 2

Colfax IC, not North Hollywood IC

LAFD and LAPD use tactical call signs

Tactical Call Signs tells the listener who you are, and what you are doing.

Tactical Call Sign exercise:

Pick an IC

IC picks and names an IC post

IC picks and names and Ops Officer

Ops Officer names tactical groups.

Message Traffic – Messages passing through a radio system are called Traffic

Observe

Think

Engage brain before using finger

Organize a concise message

Almost all emergency communications can be made in 25 words or less,

sometimes much less.

LISTEN to the channel

Is the frequency Clear?

Call To the person ‘this is’ your Tactical Call Sign

Did your recipient answer?

If not, wait 30 seconds and repeat the call – they may be busy

Call the recipient – Colfax IC this is Colfax Search 2

Recipient always called first

YOU to listen to ME = Just like in real life “Fred, can you hear me?”

Recipient hears their name or tactical and starts listening for your

message

Transmit

Report ONLY what you see and understand.  Do NOT GUESS or SPECULATE.

Make sure you fully size up the situation and update your situation as necessary.

If the situation changes, sent an updated message.

And keep in touch – every 10 minutes or less regardless

Let the IC know as additional resources arrive and as the situation

changes.

Learn good radio habits by listening to professionals on Scanner Radio or Computer

App:    Scanner Radio

Computer:  Broadcastify.com

Placitas FD radio story if not already told.

Notes for the Introduction to FRS Radios and CERT Tactical Communication

Class 2 of 2  December 17, 2013

[Repeat Privacy Codes, Tactical Call Signs, Listen, Location, and Sizeup from Class #1 as below]

Privacy Codes:

“Locks” the radio to a select group of users using the same code.

Convenient for Disneyland, but not emergency situations

Interferes with tactical communications

Can’t tell if you are ‘doubling’ with another transmission

DON’T use privacy codes –

Prevent you from finding a clear frequency

Prevents you from hearing situational reports

May cause you to ‘double’ with another communicator

Explain how to turn everything OFF

Tactical Call Signs

Use Descriptive Unique Tactical Call Signs

NOT -- CERT 1, TEAM 1, etc.

BE SPECIFIC – Be UNIQUE -- Adams Street CERT 1,  Adams Street Search 2

Colfax IC, not North Hollywood IC

LAFD and LAPD and most emergency responders use tactical call signs

Tactical Call Signs tells the listener who you are, and what you are doing

LISTEN to the channel

Call the recipient – Colfax IC this is Colfax Search 2

Alert someone you want to talk to them just like in real life “Fred, Listen to

me…:

Recipient always called first, then tell them who you are

Location, Location, Location

Height trumps power

Direct TV example

Sizeup

What is wrong?

What needs to be done?

Who needs to do it?

and

What has changed since the last transmission

What is the resolution?

Why sizeup?  Your IC finds out what is happening and can plan a response

EVERYONE else learns what’s going on and can plan accordingly.

Networks

Open Net –

Used for casual conversation

Used as “Talk around”

Keep in touch with your team on your team frequency

Pro --

Round Robin

Everyone takes a turn and gets a chance, maybe

Everyone gets to change the conversation

Con

Sometimes hard to get in

Weak stations often masked, or ignored

Some operators like to hear themselves talk and monopolize the

conversation

Easy to get off topic

Important messages may have to wait for a clear frequency

Directed Net

Net Control Operator (CERT Comms officer at IC)

Net Control Operator Directs Traffic

All calls for anyone on the Net go to the NCO first

Colfax CERT IC this is Colfax Search 1 with traffic for CERT Search 2

[CERT IC] Go with your traffic

PRO

Organized

Minimal traffic, minimal use of bandwidth

Easy to get in – Weak stations get heard

Easy to stay on topic (Net Control can make sure of this)

Very efficient for message traffic

Important message get high priority

Con

Requires Net Control

Requires operators to pay attention and follow the rules

Stations may need to wait their turn, but…

Break

“Break” is a term used when you need to get into a radio frequency that is currently busy, or is being monopolized by a user

“Break, Break” for emergency traffic

Radio Etiquette

Call the station you are calling, then introduce yourself

Why?  They hear their tactical call sign and know to pay attention.

“Colfax CERT IC this is Colfax Search 1”

Listen before you speak – always wait for a clear channel.

Ask if the frequency is clear – Is this frequency clear?  If yes, continue.  If not,

change to another frequency

Think before you talk

Extremely important

Why are you calling?

What is the most important thing you need to get across.

Easy to get confused and make mistakes when under stress

Press the PTT switch

Speak calmly and clearly

Don’t shout

Hold the radio 4 inches from your mouth and speak ACROSS it, not into it

Release the PTT switch

Wait for a response.  Unless it is an Emergency message (see below) wait 30 to

60 seconds before you try again.  The station you’re calling may be busy.

When you get a response

“Colfax Search 1 this is Colfax CERT IC go with your traffic”

Deliver your message

Be prepared to repeat

Make sure you can hear your radio.

Clip near your ear

Use earpiece (recommended)

Don’t carry it where the PTT button could be pushed

“Open Mike” Monopolized the channel

Will deplete your batteries

Messages

Get oriented

Where are you?

You know where you are, but your listeners don’t

Which way is North?

What is the name of this street?  That street?  Are you sure?

What is the address?  Is it exact or approximate?

What is the reason for the message?

You know what is happening at your location, but your listeners don’t.  Why do you need to send them a message?  What do they need to know?

What kind of information do you need to transmit?

Emergency? – Life and death

“Colfax CERT IC this is Colfax Search 1 with Emergency Traffic

“Single Family residence 12345 Colfax at Collins, flames showing,

persons trapped second floor”
	Priority? – Time sensitive, important

Routine? – Routine

Compose short, concise messages

Most important emergency messages can be 15 words or less, certainly no more

than 25.  Longer message should be thought through again or broken into

multiple messages.

Use the NATO Phonetic Alphabet for words that are difficult to spell or may be

difficult to understand.

Say “I spell” prior to launching into the NATO Alphabet.

“I Spell” November Alpha Tango Oscar = Alphabet

When transmitting numbers, say each number individually and precede by saying

“Numbers”

“Numbers One Two Three Four Five” (not 12 thousand 3 hundred forty-five)

Never use Slang, or code like “10-4”

Code and slang takes on different meanings in different jurisdictions and

becomes useless in a multi-agency operation.  Use Clear Talk or Plain English.

Started by Chief Brunicini in Phoenix and had been picked up nationwide.

Codes started with older AM transmissions when information often needed to be

repeated multiple times due to static and man made noise.	 FM

transmissions used today have better fidelity and less noise.

Plain English using simple words is always appropriate and always the easiest to

understand.

Practice Messages

Always include “THIS IS A DRILL” with all practice transmissions

Practice Message 1

Colfax CERT IC this is Colfax Search 1 with Emergency Traffic

“Single Family residence 12345 Colfax at Collins, flames showing, persons trapped second floor”

THIS IS A DRILL

Practice Message 2

Colfax CERT IC this is Colfax Search 1 with Priority Traffic

Neighbor at 12345 Colfax reports disabled person lives at this address.

THIS IS A DRILL

Practice Message 3

Colfax CERT IC this is Colfax Search 1 with Priority Traffic

12345 Colfax -- small plane crashed into the rear of house.  Fuel leaking.

THIS IS A DRILL

Practice Message 4

Colfax CERT IC this is Colfax Search 1 with Priority Traffic

LAFD on scene 12345 Colfax.  Capt. Apichatpong requsts Capt. Agbaje meet him 12345 Colfax.

Capt. [I spell] Alpha Papa India Charlie Hotel Alpha Tango Papa Oscar November Golf

Capt.[I spell] Alpha Golf Bravo Alpha Juliet Echo

(See NATO Phonetic Alphabet)

Practice Message 5

Colfax CERT IC this is Colfax Logistics with Routine traffic

Shelter at North Hollywood Rec Center reports 257 [numbers two five seven] persons signed in, more waiting

Water for 125 [numbers one two five] more persons

47 [numbers 47] blankets

39 [numberss 39] cots

Practice message 6

Colfax CERT IC this is Colfax Logistics with Routine traffic

LAPD Sergeant Godynyuk requests 17 traffic barricades and 15 traffic cones and 1 roll of Caution tape at 12345 Collins Avenue at Colfax Avenue.

Practice message composition 1

You arrive at the off ramp from the Northbound 170 and Burbank and find a large SUV CA License Number 5YSG019 upside down and heavily damaged.  Fuel is leaking from the gas tank.  Something white is rising from the engine compartment.  All of the paint is scraped off of the driver’s side. Suitcases and duffle bags are broken open and children’s clothing is strewn about.  A damaged wheelchair lies forlornly in the middle of the intersection.  A man crawls out the driver’s window and starts screaming.  There are women and children trapped inside the car, some are screaming, some are still.  Many are still strapped in seat belts.

Intersection of the 170 Northbound off ramp and Burbank Blvd. Motor Vehicle accident multiple casualties. Persons trapped.  Fuel  leaking.

Practice message composition 2

Your are Colfax Search 1 and you are searching North on Colfax and you smell smoke.  The wind is coming from the Northeast.  As you proceed the smell of smoke gets stronger and you start smelling natural gas.  You arrive at Collins Street and the smell of smoke seems to be coming from your right.

Colfax CERT IC this is Colfax Search 1

Smoke and natural gas in the area Colfax and Collins.  Permission to search East on Collins.

Practice message composition 3

It’s a lovely Sunday afternoon and you are riding your bike through an unfamiliar neighborhood.  While crossing through the intersection of Collins Avenue and Irvine Avenue you smell a strong odor of natural gas.  After you pass through the intersection you realize that it was stronger than just sewer gas, so you ride back.  The odor is strongest in the center of the intersection and you are not particularly near any houses or gas meters.  The nearest house is 50 years away.  There is a slight breeze coming from the West so you ride around the intersection several times and realize that the odor is not coming from the West, it seems to be coming from the intersection.

Practice message composition 4

You performing Community Patrol and you are driving East on Collins Avenue and you see two young men jumping over the fence from a side yard, empty handed.  They are wearing matching blue work shirts and blue jeans and are met by a heavily tattooed young man, also in a blue work shirt and blue jeans, carrying a clipboard.  All three men start walking South on Beck Street.  Two of the young men start knocking on doors on either side of the street as the third young man makes notes on his clipboard.  None of them are carrying brochures, or advertising leaflets – just knocking on doors as the third man in the street makes notes.

Practice message composition 5

There has been a minor earthquake and you and another CERT member are walking along Burbank Boulevard searching for damage.  The CERT IC is at Fire Station 60 at Chandler and Colfax.  As you pass the North Hollywood Police Station you notice the 170 Freeway overpass appears to be unsafe.  It is vibrating and small chunks of concrete are falling from it as vehicles continue to pass over it.  What should you do?

Test Message 1

A decade before the publication of Alice's Adventures in Wonderland, Lewis Carroll wrote the first stanza to what would become Jabberwocky while in Croft on Tees.

Test Message 2

She sells sea shells at the Seychelles sea shore

Test Message 3

Structure Fire 7099 Matilija Avenue cross Madeila Avenue

The NATO phonetic alphabet, more accurately known as the International Radiotelephony Spelling Alphabet and also called the ICAO phonetic or ICAO spelling alphabet, as well as the ITU phonetic alphabet.  The final choice of code words for the letters of the alphabet and for the digits was made after hundreds of thousands of comprehension tests involving 31 nationalities.  Used by the US and British Military since 1956

Use the words “I Spell” before using the NATO phonetic alphabet.  Use the word “numbers’ before using single numbers.

| A | Alpha |
| --- | --- |
| B | Bravo |
| C | Charlie |
| D | Delta |
| E | Echo |
| F | Foxtrot |
| G | Golf |
| H | Hotel |
| I | India |
| J | Juliet |
| K | Kilo |
| L | Lima |
| M | Mike |
| N | November |
| O | Oscar “Os-kah” |
| P | Papa “pa-PAH” |
| Q | Quebec “Ke-beck” |
| R | Romeo |
| S | Sierra |
| T | Tango |
| U | Uniform |
| V | Victor “Vicktah” |
| W | Whiskey |
| X | X-ray |
| Y | Yankee |
| Z | Zulu |