| L1. Incident Name LAFD AVL Installation | 2. Operational Period (Date/Time) Tuesday, June 25, 2013 | UNIT LOG ICS 214-CG |
| --- | --- | --- |
| 3. Unit Name/Designators ACS Install Team 2 | 4. Unit Leader (Name and ICS Position) K Nida, B/C and IC |
| 5. Personnel Assigned |
| NAME | ICS POSITION | HOME BASE |
| Bill Hopkins | Comms | ACS |
| Jonathan Zimmerman | Comms | ACS |
| 6. Activity Log Page 1 of 1 Pages |
| TIME | MAJOR EVENTS |
| 0830 | Met at Old 77s for briefing and equipment |
| 0945 | Called FS 7. Capt. Zimmerman says E7 in shops, Reserve engine has no GPS antenna |
| 1015 | FS75 – Arrived per conversation with Capt Romas to find company out on incident |
| 1045 Revised | FS91 – Arrived per conversation with Capt. Cameron to find company out on incident. ***Company returned to Qtrs with E91R – no GPS. E91 at Shops |
| 1115 | Returned to FS 75 - Company in Qtrs. Capt Romas says E475 permanently quartered at 77s |
|  | Removed CF-29 LT 002 0126 from T75 and replaced with CF-30 LT 0002 0276 successfully Removed CF-30 LT 0003 0041 from E275 and replaced with CF-29 0002 0143 successfully Checked R675 – LT 0001 7866 will not connect to TX Msg. Tried two other units and none would connect to TX Msg. Left original unit in R675 and advised Capt Romas to call Mobile Repair per B/C Nida |
| 1300-1330 | Lunch |
| 1330 | Called Capt. Dameron at FS 24. Says E24R in Qtrs. |
| 1400 | Arrived FS 24. E24R has a corroded and misaligned docking station with poor connections to the computer and a screen brace frozen in place. CF-30 LT 0002 0280 TX Messenger working. Tried two updated computers and none of them could find a GPS port. Checked the GPS antenna and it is in place but was unable to verify wiring. We suspect the connector in the docking station. E24R left on call before install completed so we tried to update R624 in which TX Messenger reported ‘Invalid Unit Number’. Yo says this means a unit number has not been assigned by Metro. Tried installing two different MDTs and none could find the GPS port. Verified the GPS antenna was on the unit, but were unable to trace the wiring and were unable to find a modem, which might be the problem. Left original MDT in R624. E14R returned and reported MDT failure due to dead battery. Suspect docking port. Installed rerouted power cable to MDT as before and it works. |
| 1630 | Returned to Old FS 77 with equipment for debrief and planning. |
| 1800 | Dismissed |
| 7. Prepared by: Date/Time Jonathan Zimmerman ACS 14-137 Tuesday, June 25, 2013 1030 hrs |